## Slide 1
SOME/IP introduction
  What & Why ?
  Comparison
SOME/IP run over Ethernet
  Ethernet automotive
  Unicast
  Mutilcast
Vsomeip (an implementation of the SOME/IP protocol)
  Message Format
  Service-Discovery
  Request/Response/pub-sub
Vsomeip + CommonApi
  RPC (Remote proceduce call)
Demo & Q&A
Vsomeip
Presenter the.vu@lge.com, Ha Noi 2025-10-03
Notes: Here's a comprehensive presentation structure for vsomeip:
vsomeip Presentation Outline
1. Introduction & Overview (5-7 slides)
What is vsomeip?
  Open-source SOME/IP implementation
  Developed by BMW Group
  C++ library for automotive communication
SOME/IP Protocol Basics
  Scalable service-Oriented MiddlewarE over IP
  AUTOSAR standard
  Service-oriented communication for automotive ECUs
2. Architecture & Components (8-10 slides)
vsomeip Stack Architecture
  Application Layer
  vsomeip Library
  Network Layer (TCP/UDP)
Key Components:
  Routing Manager
  Service Discovery
  Event/Notification System
  Request/Response Pattern
Communication Patterns:
  Client-Server
  Publisher-Subscriber (Events)
  Fire & Forget
3. Configuration Deep Dive (6-8 slides)
JSON Configuration Structure
Network Settings (unicast, multicast)
Service Definitions
Application Registration
Logging & Debugging Options
Service Discovery Settings
4. Service Discovery (4-5 slides)
What is Service Discovery?
Automatic vs Static Configuration
Multicast Announcements
Service Offers & Finds
When to Enable/Disable SD
5. Events & Notifications (5-6 slides)
Event-based Communication
Eventgroups & Subscriptions
Field vs Event Types
Reliable vs Unreliable Events
Multicast Event Distribution
6. Practical Examples (8-10 slides)
Hello World Service/Client
Configuration Examples
Code Snippets:
  Service Implementation
  Client Implementation
  Event Handling
Common Patterns & Best Practices
7. Debugging & Troubleshooting (4-5 slides)
Logging Levels & Output
Network Analysis Tools
Common Issues:
  Service Discovery Problems
  Event Subscription Issues
  Network Configuration
Wireshark Analysis
8. Advanced Topics (6-8 slides)
Security Considerations
Performance Optimization
Integration with Other AUTOSAR Components
Docker/Container Deployment
Testing Strategies
Production Deployment
9. Comparison & Alternatives (3-4 slides)
vsomeip vs Other SOME/IP Implementations
When to Use vsomeip
Integration with DDS, ROS, etc.
Pros & Cons
10. Demo & Q&A (5-10 slides)
Live Demo:
  Service startup
  Client connection
  Event notifications
  Configuration changes
Common Questions
Resources & Documentation
Practical Demo Ideas:
Basic Hello World: Show service/client communication
Event Notifications: Demonstrate publish/subscribe
Service Discovery: Enable/disable and show differences
Network Analysis: Use Wireshark to show SOME/IP packets
Configuration Impact: Change settings and show effects
Supporting Materials:
Code examples from your vsomeip-example project
Network packet captures
Configuration file templates
Troubleshooting checklists
Would you like me to elaborate on any specific section or help you create detailed content for particular slides?

## Slide 2
SOME/IP introduction : What ?
SOME/IP (Scalable service-Oriented Middleware over IP) is a middleware protocol designed for service-oriented communication over IP networks. (https://some-ip.com/ ). It was designed from beginning on to fit devices of different sizes and different operating systems perfectly. This includes small devices like cameras, AUTOSAR devices, and up to head units or telematics devices
SOME/IP remained as a proprietary protocol, originally developed and published by BMW Group for internal use and later shared publicly.
vsomeip is an open-source implementation of the SOME/IP protocol developed by Vector Informatik (https://github.com/COVESA/vsomeip )
Notes: https://some-ip.com/papers/2024-AEC_Ampere_TechnicaEngineering_-_SOMEIP-next-10-years_final_v1.1a.pdf

## Slide 3
SOME/IP introduction : What ?
OSI Layer | SOME/IP Role
Layer 7 – Application | Defines the services, methods, and data structures used in communication (e.g., RPC calls, service interfaces).
Layer 6 – Presentation | Handles data encoding/decoding, serialization, and marshalling of complex data types (e.g., using CDR or custom formats).
Layer 5 – Session | Manages service discovery, session establishment, and lifecycle management of services (via SOME/IP-SD).
Notes: https://www.iqpc.com/media/9048/29408.pdf

## Slide 4
SOME/IP introduction : Why ?
CAN
1986
LIN
MOST
Flexray
SOME/IP run over Ethernet
1990
2000
Ethernet
(BroadR-Reach)
2010
Engine Control Module (ECM)
Transmission Control Module (TCM)
Brake Control Module (ABS/ESC)
Airbag Control Unit
Body Control Module (BCM)
Steering Control Module …
real-time control, robust
Up to 1 Mbps
Window Lift ECU
Seat Adjustment ECU
Mirror Control ECU
Sunroof ECU …
low-speed, low-cost
Up to 20 Kbps
Infotainment Head Unit
Audio Amplifier ECU
Rear Seat Entertainment ECU
Navigation ECU
Display Control ECU …
infotainment and multimedia
Up to 150 Mbps
Brake-by-Wire ECU
Steer-by-Wire ECU
Chassis Control ECU …
safety-critical and
time-deterministic
Up to 10 Mbps
Diagnostic tool
ADAS ECU
Camera ECU
Radar/LiDAR ECU
Telematics ECU (OTA updates, cloud services) …
high-bandwidth, scalable communication
in modern architectures
Up to 100 Mbps – 10Gbps
ECU communication protocols in automotive
TSN Ethernet
2015
Autonomous driving domain controller
Sensor fusion ECU (LiDAR, radar, camera)
Brake-by-wire ECU …
Real-time, deterministic,
safety-critical, high-speed
SOME/IP was developed because of:
  Ethernet Adoption in Automotive
  Need for Service-Oriented Architecture (SOA)
In modern automotive systems, the most commonly used CAN, LIN, Ethernet, why ?
Layer 1,2
Notes: https://www.iqpc.com/media/9048/29408.pdf
list down basic ECU in automotive according protocol history: CAN, LIN, FlexRay, MOST, Enthernet, someip, TSN Ethernet
Pre-2010: Ethernet was used in diagnostics and testing tools, but not in production vehicles.
Traditional networks like CAN, LIN, and FlexRay dominated.
2011: Broadcom introduced BroadR-Reach, a 2-wire Ethernet standard tailored for automotive.

## Slide 5
SOME/IP introduction : Why ?
Ethernet-Based Protocol Comparison
Protocol (layer 5~7) | Architecture | Real-Time Support | Service Discovery | Use Case
SOME/IP (a lightweight binary protocol over TCP/UDP) | Service-Oriented (SOA) RPC (Remote Procedure Call) | ⚠ Limited (via TSN) | ✅ SOME/IP-SD | ECU-to-ECU communication, AUTOSAR Adaptive, infotainment, ADAS
DDS | Publish-Subscribe | ✅ Strong (QoS) | ✅ Dynamic | ECU-to-ECU communication, Autonomous driving, robotics, safety-critical systems
gRPC (built on HTTP/2 + Protocol Buffers) | Service-Oriented (SOA RPC (Remote Procedure Call) | ⚠Limited | ❌ Manual or via registry | Vehicle to backend services, Cloud-native services, infotainment
MQTT | Publish-Subscribe | ❌ Weak | ❌ Broker-based | Vehicle-to-cloud telemetry, diagnostics
REST over HTTP | Request-Response | ❌ Not real-time | ❌ Manual | Vehicle to Web services, connected car platforms
Both gRPC and SOME/IP follow a Service-Oriented Architecture (SOA) model, but their design goals and environments
are quite different. gRPC is less performant and heavier for embedded ECUs, ideal for backend/cloud communication
DDS offers better real-time performance than SOME/IP, but SOME/IP is more lightweight and better suited for
AUTOSAR
Notes: https://www.iqpc.com/media/9048/29408.pdf
list down basic ECU in automotive according protocol history: CAN, LIN, FlexRay, MOST, Enthernet, someip, TSN Ethernet
Pre-2010: Ethernet was used in diagnostics and testing tools, but not in production vehicles.
Traditional networks like CAN, LIN, and FlexRay dominated.
2011: Broadcom introduced BroadR-Reach, a 2-wire Ethernet standard tailored for automotive.

## Slide 6
2. SOME/IP run over Ethernet
Automotive Ethernet (BroadR-Reach)
BroadR-Reach is a specialized Ethernet physical layer standard developed for automotive applications.
It was originally created by Broadcom
Feature | Traditional Ethernet | BroadR-Reach
Cable Type | Rj45(8 wires) | Single twisted pair (2 wires)
Cable Length | Up to 100 meters | Up to 15 meters (UTP), 40m (STP)
Duplex Mode | Full-duplex | Full-duplex
Weight & Cost | Heavier and more expensive | Lighter and cheaper
Convert Automotive Ethernet <-> Traditional Ethernet: Media Converter
Notes: https://www.accuratetechnologies.com/blog/post/automotive-ethernet-vs.-regular-ethernet

## Slide 7
2. SOME/IP run over Ethernet
Automotive Ethernet: Topology
Ethernet PHY
ECU1
Ethernet PHY
ECU2
Ethernet PHY
ECU3
Ethernet PHY
ECU4
Daisy chain topology (less common): is often used in cost-sensitive or space-constrained design.
Disadvantages : If one ECU or link fails → breaks the chain, harder fault isolation and timing control
Star topology (most common today): used in most current automotive Ethernet architectures
Advantages:
Simple management
Easier diagnostics (one link failure doesn’t affect others)
Supports mixed networks (Ethernet ↔ CAN, LIN, FlexRay via gateway)
Disadvantages:
Requires more cabling to the central switch
Slightly higher cost due to extra switch port count
Switch
ECU1
ECU2
ECU3
ECU4
Notes: https://www.accuratetechnologies.com/blog/post/automotive-ethernet-vs.-regular-ethernet

## Slide 8
2. SOME/IP run over Ethernet
Unicast (TCP/UDP)
Switch1
Switch2
PC 1
PC 2
PC 3
PC 4
192.168.1.3/24
192.168.1.4/24
192.168.1.5/24
192.168.1.6/24
Send to 192.168.1.4
Send to 192.168.1.5
If PC1 wants to send the same data to PC2 and PC3,
it must send two separate packets:
PC1 → PC2 : Packet #1
PC1 → PC3 : Packet #2
➡️ This means:
2 copies of the same data are transmitted.
Bandwidth usage doubles for each additional receiver.
The sender’s CPU must process multiple send operations.
Mutilcast is better for this case
Notes: https://www.accuratetechnologies.com/blog/post/automotive-ethernet-vs.-regular-ethernet

## Slide 9
2. SOME/IP run over Ethernet
Mutilcast (UDP only)
Switch1
Switch2
IGMP Join multicast
239.1.1.1
IGMP join multicast
239.1.1.1
Multicast Group | Forward to ports
239.1.1.1 | Port_PC2, Port_trunk_to_Switch2
Multicast Group | Forward to ports
239.1.1.1 | Port_PC3, Port_trunk_to_Switch1
Switch 1 update multicast forwarding table
Switch 2 update multicast forwarding table
IGMP Snooping
PC 1
PC 2
PC 3
PC 4
192.168.1.3/24
192.168.1.4/24
192.168.1.5/24
192.168.1.6/24
PC2 and PC3 join a multicast group (239.1.1.1),
they will receive any data sent to that multicast IP address
— as long as the network infrastructure supports multicast forwarding.
Notes: https://www.accuratetechnologies.com/blog/post/automotive-ethernet-vs.-regular-ethernet

## Slide 10
2. SOME/IP run over Ethernet
Mutilcast (UDP only)
Switch1
Switch2
Multicast Group | Forward to ports
224.224.224.245 | Port_PC2, Port_trunk_to_Switch2
Multicast Group | Forward to ports
224.224.224.245 | Port_PC3, Port_trunk_to_Switch1
Switch 1 update multicast forwarding table
Switch 2 update multicast forwarding table
Send to 224.224.224.245
forward
forward
forward
When PC1 sends data to a multicast IP address (224.224.224.245),
and PC2 and PC3 have joined that multicast group, they will receive the same data.
Notes: https://www.accuratetechnologies.com/blog/post/automotive-ethernet-vs.-regular-ethernet

## Slide 11
3. Vsomeip
SOME/IP Message Format
The following picture shows the general structure of a SOME/IP SD message.
In principle, SOME/IP communication consists of messages sent between devices or subscribers over IP.
Notes: https://github.com/COVESA/vsomeip/wiki/vsomeip-in-10-minutes

## Slide 12
3. Vsomeip
Service-Oriented Architecture (SOA)
Vsomeip lib
Vsomeip lib
RoutingManagerd impl
Vsomeip lib
Vsomeip lib
Vsomeip lib
App4 impl
Device1(192.168.1.3/24)
Device2(192.168.1.4/24)
Vsomeip lib
RoutingManagerd impl
Ethernet
service-discovery
(Offer/Find Service)
request/response/
publish-subscribe
Local socket (UDS)
Local socket (UDS)
Mutilcast {
IP: 224.224.224.245
Port: 30490
}
The RoutingManagerd (Middleware deamon) is responsible for:
Routing service messages between applications on the same device.
Forwarding messages between devices over Ethernet.
Managing service discovery and subscription handling.
There is only one routingmanagerd per device/host.
vsomeip.json define multiple critical purposes in the vsomeip architecture (include ServiceA identifier, ServiceA endpoint)
App3 impl
Service A
Service B
Discoverability: Find services dynamically
…
App ID = 0x1212
App1 impl
Service C
Client A
App2 impl
Client C
Client A
ServiceA endpoint{
TCP port= 30500
UDP port = 30501
}
ServiceA identifier {
service ID = 0x1234
instance ID = 0x5678
}
ClientA don’t know Device2 (IP + TCP/UDP Port)
ClientA only know ServiceA identifier (service ID + instance ID).
Q: How client A can send data to Service A ?
/tmp/vsomeip-0
/tmp/vsomeip-1212
Notes: https://aws.amazon.com/what-is/service-oriented-architecture/
https://github.com/COVESA/vsomeip/tree/master/documentation

## Slide 13
3. Vsomeip
Service-Discovery (Offer/Find Service)
src: 192.168.1.3:30490
dst: 224.224.224.245:30490 (mutilcast address)
FIND Message {
serviceId: 0x1234
instanceId: 0x5678
...
}
Notes: https://aws.amazon.com/what-is/service-oriented-architecture/
https://github.com/COVESA/vsomeip/tree/master/documentation